## Slide 1: Packet Radio
By Peter Tryon
VA7PWT

## Slide 2
What It's All About
Packet seems to offer something different from other facets of Amateur Radio, yet it can be used for everything from a local QSO to a DX contact thousands of miles away, for electronic mail, message transmission, emergency communications, or just plain tinkering in the world of digital communications.

## Slide 3
A ham can get involved very easily with relatively small out-of-pocket expenses. All you need is a transceiver, a computer, and a TNC or special packet modem and software. Packet can be used on all Frequencies but mostly on 2 meters VHF. You probably already have the rig and the computer, so all you need to buy is the TNC.

## Slide 4
There are mainly two types of interface units used to connect your radio to a computer to send data out over the air. The first one I will show is the more standard TNC that has been used for many years. These are more familiar to the older Amateur radio operator. Today, however, with modern technology, the digital world is expanding. The new interface is being used as the older TNC style will not handle the new Digital forms of communication. The Sound Card Interface has been introduced.
Types of interface units

## Slide 5
The TNC, the Terminal Node Controller, is wired between the computer and the radio. It contains software for controlling the outgoing and incoming transmissions for your station and a modem that converts the data from the computer into AFSK tones for transmission and changes the tones that are received by the radio into data for the computer.
Terminal Node Controller

## Slide 6
Packratt 232 TNC
Kantronics 3 plus TNC
Two of the more common TNC used

## Slide 7
Sound Card Interface
This is basically just the modem part of the TNC. There is no embedded processor and usually some simple circuitry for triggering the push-to-talk.
To do Packet with a Sound Card Interface, you need software on your computer that provides the software included in the TNC, including the telnet interface. The sound card built into you PC can do most of these same functions, though most external interfaces have AC coupled sound cards, isolating the PC. The advantage of a Sound Card interface is they have built in PTT circuitry and work with your transceiver. Most vendors also provide the cabling to fit you transceiver. If using a PC’s internal sound card, you must devise your own transceiver interface for PTT with some form of Isolation.

## Slide 8
The advantage of the sound card interface type is all the commands that you normally have to use for a Serial style TNC are all included in the Terminal programs you use to chat on packet or Winlink. The other advantage is the programs for use on HF are mostly designed for the Sound card interface style now. The introduction of the sound card interface has made communication much easier and cheaper.
I will later on in this presentation show the ease and difference in the set up of both.

## Slide 9
Three different types of Sound Card Interfaces. The SignaLink is the most commonly used

## Slide 10
This is UZ7HO type of Sound Modem for a single program. I will show later a sound modem that allows you to run multiple programs at same time

## Slide 11
What’s A Packet?
A Packet is a group of bits (binary digits) structured and standardized that has contained within it the addressing information, message, error-checking and control information. The information is organized into a Frame (A Packet). A Frame is a set sized template for sending information. The Amateur X.25 protocol is the manner in which we send frames. Both the sending and receiving TNC is programmed to encode into frames to be sent, and decode received frames.
Each Frame (Packet) can send up to 256 characters in each Frame (Packet).That is close to 3 lines in a sentence. If the information to be sent is more than 256 characters, then it is broken up in to the amount of Frames (Packets) needed to send the message. Once the first Frame (Packet) is received , a command is sent to have the next Frame (Packet) sent. This continues until entire message has been received.

## Slide 12
What is an SSID?
(Secondary Station Identification)
Callsign-1 through Callsign-15
Usually your callsign by itself is considered callsign-0. By some standards, using a ssid of 1 denotes your mailbox. You may have up to 16 of your callsign active at any one time, each with a unique number identifier (SSID). No duplicates are allowed at any one time

## Slide 13
An SSID (Secondary Station Identifier) is a number following a station's callsign. The numbers range from -0 to -15 and are used to identify the type of packet service the station is running. -0 Home station (note: "-0" not needed - automatically presumed if no SSID.) -1 Home station personal mailbox (usually a TNC-based PBBS). -2 Gateways -3 Full service BBS's (those that forward mail and bulletins). -4 Network Nodes (having two or more radio ports that perform routing functions via TCP/IP, NetROM, etc.) (Can be combined with BBS's that also perform routing.) -5 Console, keyboard or printer -6 Conference Bridges -7 Crossband digipeaters (and KA-Nodes) -8 Crossband digipeaters -9 Mobiles -10 Winlink 2K -11 unassigned -12 unassigned -13 unassigned -14 unassigned -15 Often used as a downlink address when exiting the far end of a network connection. (Explained later)

## Slide 14
Cross-band digipeater: This device receives a signal on one frequency band and retransmits it on another. This capability is particularly useful for extending the range of communication across different frequency bands, allowing for more flexible and widespread communication.
Node -8: A node with the suffix -8 can indicate it is, a digipeater that is part of a network. Nodes can perform various functions, including routing packets, acting as gateways to other networks, or providing additional services like messaging, APRS tracking, or weather updates.
Node -10: This indicates it will connect you to the internet via the Winlink system
Explanation of a few of the main ones you will see Beaconing

## Slide 15
Why does my call sign change to a -15 designation when using a Digipeater
So, the “-15” designation typically indicates that your station is an additional station, which could be used for various purposes not specifically covered by other SSIDs
Basically the digipeater gives this designation to you so it knows who you are. This is a fictitious call sign. Do not make a call to this.
For example. I go through VE7TXD-8 and connect to VE7KHI (Keith on Hornby Island). What you would see is :-
VA7PWT-15 to VE7KHI
If Keith wanted to connect to me he would call VA7PWT not the VA7PWT-15
.

## Slide 16
New things that you can do to make your Packeteering easier and more fun.
-Multiple contacts at same time
-Your own Personal Mailbox
-Run multiple programs at same time
I have noticed during our Packeteering night a lot of you do not know about these.
In the following slides I will introduce you
to these.

## Slide 17
Check your TNC commands in your operator manual for the TNC you are using
Multi-Connects on the KPC-3
The TNC makes it possible for you to talk to more than one person at the same time. Single port TNCs such as the KPC-3 Plus support 26 streams on the one port.
The command MAXUSERS determines how many streams may be used at one time, per port.
Command USERS determines how many people can connect to the TNC per port. An incoming connect uses the next available stream.
However, if MAXUSERS is set larger than USERS, you can still issue outgoing connects on additional streams.

## Slide 18
To change streams ( to make another connect or to send data to another station already connected to you) just hit SHIFT| and letter of channel you wish. ( E.g. Shift|B) this will change you to channel B.
When someone connects with you ,you will see channel letter and then their call sign (eg A VA7PWT ). If another person connects with you, again you will see (eg B VA7AYW). So to talk to each just follow above. Each time they send a packet message to you, you will see their call with the channel letter.
To determine which port you are on, simply use the STATUS command, typing STAT at the command prompt. The TNC will report which streams are active and which one you are on.
If you wish to remain on the current stream to communicate, no action is necessary.
Multi-Connects on the KPC-3 Continued

## Slide 19
Connect to Your Mailbox
Step 1. Go to COMMAND mode (if you are not already there), where you will see the “cmd:” prompt.
Step 2. Type CONNECT (letter c) call (where “call” is your MYPBBS) and press the ENTER (return) key. By default, MYPBBS is the callsign you entered right after the autobaud routine, with “-1" appended to it. Note: To see the current mailbox callsign, type MYPBBS at the CMD prompt and press the ENTER (return) key. The callsign shown is the one to use when connecting to your mailbox (PBBS)
If for some strange reason it was not applied just enter at cmd prompt MYBBS (your call sign). For example (MYBBS VA7PWT) then hit enter button.
Then try Step 2 again.

## Slide 20
Step 3. Your KPC-3 Plus will connect you to the mailbox. Your screen should look something like this:
cmd: CONNECT (YOUR CALL)-1
cmd:*** CONNECTED to (YOUR CALL)-1
[KPC3P-9.1-HM$] 47500 BYTES AVAILABLE IN 15 BLOCK(S)
ENTER COMMAND: B,J,K,L,R,S, or Help>
Connect to Your Mailbox Continued

## Slide 21
If you leave your Packet station running , then friends can leave messages for you. The Modem will flash a light on the front saying you have a message waiting for you.
On the next few slides I will show the ease of using a Sound modem style Terminal
As I said earlier that the new technology has made our lives much easier. All the commands are all imbedded into the programs software.

## Slide 22
Sound Modem style Multiple Channels and Mailbox Using Easyterm by UZ7HO
Multiple Channels
If you remember all the work you had to do to set up your TNC for multiple connections. Well its all done for you with the Sound modem style.
Here is your channels. When someone calls their call shows in the channel they are on. Neat thing is it shows in red when they are texting you.

## Slide 23
Setting up your Mailbox with a Soundmodem style
Click here to set up Mailbox

## Slide 24
Just fill this in with -1 or -3 after your call and hit OK
That’s it. Easy

## Slide 25
WINTNC Program by G7JJF

## Slide 26
K-commands delete messages sent by you or to you
K msg# — Deletes a message identified by its number.
KM — Deletes all the messages addressed to you, that you haven’t yet read.
L-commands list message headers
L — Lists the new messages since the last usage of this command.
Lx — List messages with status “x” – x can be D F N Y $.
LB —Lists bulletins.
LC — Lists all Bulletin “categories” (TO Fields)
LM — Lists the messages to you.
LL n —Lists the last n messages.
LR — Equivalent to L but the messages are listed in reverse order.
LT — List Traffic (NTS-messages).
L< Callsign — Lists message from [Callsign].
L> Callsign — Lists messages to [Callsign].
L@ [BBS] — Lists the messages VIA BBS.
L msg#- — Lists all messages, starting from msg#
L msg#-msg# — Lists messages between the given numbers.
BBS Command for accessing the PBBS or BBS bulletin board

## Slide 27
R-commands read messages
R msg# msg# — Reads the messages by their numbers.
RM — Reads new messages to you.
S-commands send messages
S[type] callsign — Sends a message or a bulletin; If the type is not specified, it will be sent as private.
SP callsign — Sends a private message.
S callsign @ BBSCALLSIGN — Sends a message to a station AT another BBS; The message must be terminated by a Ctrl/Z or /EX followed by a return.
SC Msg# Callsign @ BBSCALLSIGN — Copies a message or bulletin to the specified callsign.
SR Msg# — Replies to a message.
BBS Commands continued

## Slide 28
Example on how to send a message to someone using a BBS board
1- Type S (call sign of person) enter key
2- You will get back “Enter a title”
3- Enter your title (e.g. Hello) then press enter
4- you will get a message “ enter message”
5- type your message then enter
6- type/ex enter
7- you will get a message stating message has been saved with message number#

## Slide 29
Ok I have shown you the old old way of sending a message with packet. Well I have developed a Packet Mail Program that makes sending a message to a friend easy.
Check out my website for the program called VA7PWT Packet Mail Program.
All documentation to run my program is included.
HTTPS://VA7PWT.org

## Slide 34
A problem we have is trying to run multiple programs at the same time. This can be very tiring and frustrating. The way that most of us use is to close one program and then restart the next program. For example. We are familure with running a Packet terminal to chat. Then we want to use Winlink. We have to close our terminal to allow Winlink able to access the modem. If you don’t it causes a collision and neither program can access the modem.
Well thanks to modern day programing we now can run multiple programs at the same time and access the same modem without having to close one down.
Sound good
On the next few slides I will show you how to do this and its totally Safe and Free.
Starting to make your life easier

## Slide 35
For those of you using the Serial Port type of modem
First off you down load a simple program that is a serial port splitter. What this program does is it creates a virtual serial port and directs your programs all to the single port.
So lets get started
Go to website www.eterlogic.com
When it opens click on the picture

## Slide 36
Then scroll to bottom of website
Open this file

## Slide 37
Install onto you computer. It is safe to install. Once you have done that start the program by clicking on the icon on you computer

## Slide 38
Click on No

## Slide 39
click here

## Slide 40
Click here and select Splitter then hit next

## Slide 41
Click Settings and set you baud rate to 1200
Make sure you set DTR/RTS to yes then click ok
2
com1
In here it will show what com port you are using
This is your virtual com port that all your programs will use

## Slide 42
Com1 => Com2 (< this is the virtual port) Splitter Ready
This is just an example, All depends on your comports
Just shrink this down

## Slide 43
Now that we have the splitter running all you have to open up the programs you want to use and make the connection for them to the same virtual com port.
Next slide I am showing how my station looks.

## Slide 44
I have both open and just move curser to which program I need to use. No more closing and opening

## Slide 45
Sound interface style of Splitter
I use “DIREWOLF” Software
Just go onto web and download “Direwolf Packet modem”
Then just install on your computer
It is safe

## Slide 46
Open up file and click on Direwolf.conf.

## Slide 47
Once you have opened the Config. File all you have to do is edit it to fit your programs requirements. If you are running the Signalink, then all you have to do is change Mycall and the Kiss port to 8100. If not just follow the instructions or watch the video from Modernham . This guy is amazing and easy to follow.

## Slide 50
Should look like this when you open it depending on your settings. Once open just shrink it down

## Slide 51
AS you see I now have both programs running and connected to same sound card interface. No more having to shut down one to use the other.

## Slide 52
This is just the beginning of things we can do using packet. The future is ours to experiment with and except changes for ease and speed of communication.
Thank you for your time
Questions